Selection of necessary small parts (O-rings, sealing rings, gaskets +++) for major overhaul/shimming of Motor case / Rear fork / Gearbox on the big Guzzi-motors (750ccm –1000ccm)

Mainly identical parts from 1972 and until today. Check the 1100ccm-models.	CHECK YOUR OWN ARTICLE-NUMBERS BEFORE ORDERING ANYTHING		Dated: 29/09-2004

| PARTS IN THE MOTORCASE | MG art. no: | Specifications | Remarks | Tools | EUR/ea. MG part no. |  |
| --- | --- | --- | --- | --- | --- | --- |
| Gasket, front cover/motor case | 12001200 |  |  |  | 3 |  |
| Sealing ring, front cover | (90402838) 90402840 | ANGUS 28x38x7 | Replaced by 90402840 |  | 4 |  |
| Special-nut, crank shaft | 93601026 | SKF KM5 |  | Special | 6 |  |
| Locking washer, behind this special-nut | 95028025 | SKF MB5 | Should be replaced every time, due to the actual ear breaks 2-time. |  | 1 |  |
| Sealing ring, rear main crank flange | 90405367 90405367002 | ANGUS 53x68x10 VITON (Brown) | Heat resistant VITON recommended. CORTECO 53X68X10/8 w/double sealing + oil-throwaway-ring |  | 8 |  |
| Gasket, rear main crank flange | 12011800 |  |  |  | 2 |  |
| PARTS IN THE GEARBOX (5-speed) |  |  |  |  |  |  |
| Throw out bearing | 12087001 |  | Bearing + 2 washers |  | 11 |  |
| Plastic-tubes (seals), around the pusher-rod | (12085901) 14085900 |  | Replaced by 14085900 2 ea. |  | 2 |  |
| O-ring, in cover behind throw out bearing | 90706170 | OR 3068 Ø17,12 x 2,62 | Have also seen specified: Ø17 x 2,8 |  | 1 |  |
| Special-nut, on input-shaft | 93601022 |  |  | Special | 17 |  |
| Locking washer, behind this special-nut | 95028022 |  | Should be replaced every time, due to the actual ear breaks 2-time. |  | 1 |  |
| O-ring, “thin”, input-shaft | 90706235 | OR 2093 Ø23,52 x 1,78 | Between the clutch-boss and input-shaft bearing |  | 1 |  |
| O-ring, “fat”, input-shaft | 90706203 | OR 3081 Ø20,30 x 2,62 | Between input-shaft and clutch-boss |  | 1 |  |
| O-ring, “fat”, output-shaft | 90706203 | OR 3081 Ø20,30 x 2,62 | Between 1’st and 5’th gear. Early gearboxes. |  | 1 |  |
| O-ring, “thin”, output-shaft | 90706219 | Later gearboxes | Between plate over 5’th gear and plate under speedo-gear. |  | 1 |  |
| Sealing ring, in box and cover | 90403547 | ANGUS 35x47x7 | 2ea. [Alternative: 90403547001 VITON (Brown colour)] |  | 3 [10] |  |
| Shims, for selector-drum | 55235000 | 0,6mm | Order 2ea. “Nice to have” |  | 1 |  |
| Shims, for selector-drum | 55235001 | 0,8mm | Order 2ea. “Nice to have” |  | 1 |  |
| Shims, for selector-drum | 55235002 | 1,0mm | Order 2ea. “Nice to have” |  | 1 |  |
| Shims, for selector-drum | 55235003 | 1,2mm | Order 2ea. “Nice to have” |  | 1 |  |
| Spring, for selector-pawls | (14238200) 28238261 |  | Replaced by 28238260 and further 28238261 Someone recommends to replace every time the gearbox is opened. |  | 5 |  |
| O-ring, selector-pawls-shaft | 90706140 | OR 3056 | Ø14 x 2,5 |  | 1 |  |
| Bearing, in cover (+ the same in the box) (It’s the bearing in the cover, which is mostly stressed. Remember locking-plate) | 92218424 | 25x52x20,6 (2x14 in steel-housing) | INA 3205 (Used for among others: California II) SKF 3205 AC3 (Double row angle contact bearing) NTN 3205 AC3 / NSK 3205 JC3 recommended alt. by Peter Roper. (2x14 balls in metal house are better then 2x9 balls in plastic house.) |  | 54 |  |
| Locking-plate, for bearing | 14213802 14213803 | Metal (For 2 screws) Metal (For 3 screws) | 5-speed boxes before 1974 5-speed boxes after 1974 |  | 17 |  |
| Locking-plate, for bearing |  | Plastic | Don’t use this plastic plate. |  |  |  |
| Gasket, box/cover | 14201110 |  |  |  | 1 |  |
| Nut, output-shaft | 14219310 | Moment: 17kgm | Pipe: Long 27mm, with sharp entrance and angle. | Special | 6 |  |
| PARTS IN THE REAR-FORK |  |  |  |  |  |  |
| Bearing, rear-fork | (92249216) 92249217 | 17x40x12 (Conical roller) SKF 30203 J2 | Replaced by 92249217 2 ea. |  | 18 |  |
| Sealing ring, rear-fork | 90403040 | ANGUS 30x40x7 | 2 ea. |  | 3 |  |
| UNI (Ø28mm, 1972 to 1975) | 12328000 12328001 |  | Replaced by 12328001 |  | 148 |  |
| Bearing, UNI (Ø28) | 92204228 | SKF 62/28-2RS1 | 28x58x16 Recommended to replace whenever UNI is replaced. |  | 20 |  |
| Rubber-gaiter, around UNI (Ø28) | 12548000 |  |  |  | 6 |  |
| UNI (Ø30mm, 1975 and newer) | 17328050 |  | 30328030 is replaced by 17328050 |  | 130 |  |
| Bearing, UNI (Ø30) | 92204230 | SKF 6206-2RS1 | 30x62x16 Recommended to replace whenever UNI is replaced. |  | 16 |  |
| Rubber-gaiter, around UNI (Ø30) | 18548000 |  |  |  | 6 |  |